## inertial frame
roll (x-axis) rotation on longitudial axis
pitch (y-axis) rotation on lateral axis
yaw (z-axis) rotation on vertical axis
### earth centered inertial pointing from center of earth
X and Y axis fixed on equatorial plane
Z axis 90° angled to equatorial plane through poles
J2000 coordinates
defined with equator and equinox at 12:00 (noon) terrestrial time on 01.01.2000
X axis aligned to mean equinox, Y axis 90° east, Z axis aligned with Earth's spin (celestial north pole)
### IMU (inertial meassurement unit)
#### 9DOF sensor LSM9DS1
I²C interface
#### 9DOF sensor BNO055
I²C interface
internal fusion and angle calculation
#### sensor values
acceleration
gravitational force on earth surface is meassured in G - 1G=9.8m/s²
gyroscope
rotational motion meassured in dps (degrees per second)
Earth rotation 360°/86400sec (=0,0041~6 dps)
magnetometer
meassuring force of magnetic fields in Tesla or Gauss (1 Tesla = 1000 Gauss, 1000µT=1G)
Earth's magnetic field strength is 31.869µT (at 0°/0°)
## I2C bus
### general timings
clock frequency fSCL=0-100kHz; 0-400kHz
bit length tSCL=1/fSCL=0,00001s=10µs; 2.5µs