## inertial frame
roll (x-axis) rotation on longitudial axis
pitch (y-axis) rotation on lateral axis
yaw (z-axis) rotation on vertical axis
### earth centered inertial pointing from center of earth
X and Y axis fixed on equatorial plane
Z axis 90° angled to equatorial plane through poles
J2000 coordinates
defined with equator and equinox at 12:00 (noon) terrestrial time on 01.01.2000
X axis aligned to mean equinox, Y axis 90° east, Z axis aligned with Earth's spin (celestial north pole)
### IMU (inertial meassurement unit)
#### 9DOF sensor LSM9DS1
I²C interface
#### 9DOF sensor BNO055
I²C interface
internal fusion and angle calculation
#### sensor values
acceleration
gravitational force on earth surface is meassured in G - 1G=9.8m/s²
gyroscope
rotational motion meassured in dps (degrees per second)
Earth rotation 360°/86400sec (=0,0041~6 dps)
magnetometer
meassuring force of magnetic fields in Tesla or Gauss (1 Tesla = 1000 Gauss, 1000µT=1G)
Earth's magnetic field strength is 31.869µT (at 0°/0°)
## I2C bus
### general timings
clock frequency fSCL=0-100kHz; 0-400kHz
bit length tSCL=1/fSCL=0,00001s=10µs; 2.5µs
## Hardware and pinout
### ST‑4 Auto Guider
ST‑4 port is a RJ12 (6P6C modular plug) connector. The commands are transmitted active low. The current sink must be suitable for at least 25mA. For security and/or isolation purposes relais could be used instead of simple transistors.
RJ12	ST‑4 signal		hints
1	n.c.		could be VDD on some Equipment / +5V/DC on many CCD guiders
2	GND		common for all equipment
3	+RA (east, left)		active low to common ground
4	-DEC (south, down)		active low to common ground
5	+DEC (north, up)		active low to common ground
6	-RA (west, right)		active low to common ground

### Meade AutoStar
#### RS232 port on HandBox
The RS232 port is a RJ11 (4P4C modular plug) connector on the handbox. The signal is standard RS232 level with an driver chip inside the handbox.
RJ11	HBX signal	DB9f
1	RxD	3 (TxD)
2	TxD	2 (RxD)
3
4	GND	5 (GND)

Communication parameters are 9600N81, 9600 Baud, no parity, 8 data bits, 1 stop bit, no handshaking.
### Celestron
#### HC Serial Port
RS232 Serial port on handcontroller uses a RJ11 (4P4C modular plug) connector.
RJ11	HBX signal	DB9f
1	TxD	2 (RxD)	from telescope to computer
2	GND	5 (GND)
3	n.c
4	RxD	3 (TxD)	to telescope from computer

#### NexStar GPS PC port
RS232 Serial port on NexStar GPS uses a RJ45 (8P8C modular plug) connector.
RJ45	scope signal	DB9f
1	GND	5 (GND)
2	RxD	3 (TxD)	to telescope from computer
3	GND	5 (GND)
4	TxD	2 (RxD)	from telescope to computer
5	RTS	8 (CTS)	hardware handshaking
6	GND	5 (GND)
7	CTS	7 (RTS)	hardware handshaking
8	GND	5 (GND)

#### HEQ5 controller port
RJ45 (8P8C modular plug) connector used for 5V TTL level RS232 and +12V/DC power supply.
RJ45	scope signal
1	GND
2
3
4	GND
5	TxD		from telescope to computer
6	RxD		to telescope from computer
7	+12V
8	+12V

#### EQ6 controller port
DB9 female connector used for 3.3V TTL level RS232 (5V tolerant) and +12V/DC power supply.
DB9f	scope signal
1	GND
2
3
4	GND
5	TxD		from telescope to computer
6	RxD		to telescope from computer
7	+12V
8	+12V